## Slide 1: Eddy Covariance Measurement of Ecosystem Carbon Exchange
Please read:
D. D. Baldocchi. Assessing the eddy covariance technique for evaluating carbon dioxide exchange rates of ecosystems: past, present and future. Global Change Biology, 9, 479-492, 2003

## Slide 2: Turbulence

## Slide 10: Rhyme
“Big whorls have little whorls, Which feed on their velocity; And little whorls have lesser whorls, And so on to viscosity”
      Lewis Richardson, The supply of energy from and to Atmospheric Eddies 1920
“Great fleas have little fleas Upon their backs to bite 'em, And little fleas have lesser fleas, And so, ad infinitum”
      Augustus De Morgan (19th century mathematician, parodying Jonathon Swift, 1733)

## Slide 11: Mass Conservation Equation for CO2
c is mass mixing ratio (density of CO2/density of air)
(u, v, w) are components of vector wind (positive toward east, toward north, and upward)
(Fx, Fy, Fz) are components of vector mass flux of CO2
local rate of change
advection (3D)
flux divergence (3D)
biological source/sink

## Slide 12: Consider Idealized Conditions
No change in CO2 with time (term I ~ 0)
Wind is steady
Surface is horizontally homogeneous
Terrain is flat
Term II ~ 0
Horizontal fluxes don’t diverge … term III ~ 0
reference surface

## Slide 13: Turbulent CO2 Fluxes
Imagine a turbulent eddy over an active ecosystem
Updrafts are systematically depleted in CO2 relative to downdrafts
Updraft:
  w’c’ < 0
Downdraft:
  w’c’ < 0
Average over eddy:
w’c’ < 0
photosynthesizing ecosystem
w’ < 0
c ’ > 0
w’ > 0
c ’ < 0

## Slide 14: Reynolds’ Averaging
Mean of a mean is the mean
Mean of a prime is zero
Mean of a product is not necessarily zero!
0
0
means
perturbations
vertical mass flux of CO2

## Slide 15: Variance, Covariance, Correlation
mean
perturbation
variance
variance of w
covariance of w and c
Normalized covariance is the correlation coefficient
c’
w’

## Slide 16: Sonic Anemometer
Measures elapsed time for sound pulses to cross air in 3D
Speed of sound is a known function of temperature
Relative motion determined accurately in 3D
Very fast instrument response time

## Slide 17: Turbulent Flux Measurements
“Eddy covariance” methods
Measure c,T, q, and 3-D wind speed (u,v,w) very frequently
  At least 10 Hz
Subtract time means to get primes
Compute products of primes to obtain fluxes
c’
w’
t
t
Oklahoma Prairie

## Slide 18
http://www.fluxnet.ornl.gov

## Slide 19
http://www.fluxnet.ornl.gov
FluxNet Tower Sites

## Slide 20
Flux Towers

## Slide 21: Cospectra and Spectral Filtering
High-pass filtering due to slow instruments, poor instrument placement, sampling through tubing
Low-pass filtering due to slow atmospheric mixing by large eddies (many minutes) or convective clouds

## Slide 22: Violation of Assumptions
The real world is a messy place!
  Coordinate rotation
  Advective fluxes

## Slide 23: Niwot Ridge Ameriflux Site

## Slide 24: Typical Diurnal Cycle of PBL Over Land
(Stull, 1988)
Notes: Before we look into the data from the observations from the tower, I’d like to briefly describe a typical boundary layer over land.

## Slide 25: Daytime PBL Profiles
Surface is a source of heat and moisture, and a sink for momentum
Heat flux reverses sign near top of PBL due to entrainment

## Slide 26: Stable (Nocturnal) Boundary Layer
Nocturnal BL is typically quite shallow (few hundred m)
Strong cooling at surface can produce a moisture sink (dew or frost)
Decoupling from surface friction can allow nocturnal jet to form
Shear under nocturnal jet sometimes produces “bursts” of mixing

## Slide 27: Storage “Fluxes”
Nocturnal stable layer inhibits mixing of CO2 produced by soil respiration from reaching instruments, accumulates below reference height
  NEE underestimated
Solar heating during early morning releases stored CO2 in a big “burst”
  NEE overestimated
Maybe OK unless stored CO2 “leaks out” by horizontal advection or gravitational drainage flow
Try to correct for these effects by directly measuring changes in storage
turbulent flux
storage “flux”
w’c’
R

## Slide 28: Diurnal Cycles
Underestimated night-time turbulent fluxes paired with high storage fluxes
Early morning “burps” as turbulence begins paired with strongly negative storage fluxes
Time integral conserves flux only if there is no “leakage” at night due to drainage flow or advection

## Slide 29: Other Fluxes
Eddy covariance sites typically measure turbulent fluxes of
  Sensible heat:
  Latent heat:
  Momentum:
Momentum flux is also called “surface stress,” and is related to a turbulent velocity scale called the friction velocity
(W m-2)
(W m-2)
(N m-2)
(m s-1)

## Slide 30: Site Locations
+
+
FLONA
Tapajos
Reserva Jaru

## Slide 38: Can “u* Filtering” Avoid “Lost Fluxes”
Dependence of w’c’, storage, and NEE on u* at night suggests significant “lost fluxes
Implications for time-mean results?
Scott Saleska, Harvard University, personal communication

## Slide 39: Effect of u* “Correction”
Integrated over a year, u* correction changes this site from a big sink to a big source!

## Slide 40
Time (GMT)
CO2 Exchange (mmol m-2 s-1)
NEP was calculated by averaging the flux measurements across time of day and summing all hours.
The annualized flux using all the nocturnal data was -9.3 tC ha-1 yr-1.
Mike Goulden,
UC Irvine,
personal
communication
Annualized Fluxes: Tapajos National Forest, km 83 site

## Slide 41
u* (m s-1)
CO2 Exchange (mmol m-2 s-1)
Effect of calm nights
The annualized flux calculated with all the data likely overestimates C uptake since transport mechanisms during calm periods may remove CO2 by routes that are not included in the covariance (e.g., drainage).

## Slide 42
Recalculated flux using just windy periods
The annualized efflux can be recalculated only considering periods windy periods.
Time (GMT)
CO2 Exchange (mmol m-2 s-1)
u* < 0.1 ms-1
0.1 ms-1 < u*
< 0.2 ms-1
0.2 ms-1 < u*
< 0.3 ms-1
0.3 ms-1 < u*

## Slide 44
Why is the correction for calm nights so much at km83 ?
The annual calm night correction is a function of three things:
=
Nocturnal hours
with significant
respiration
(T>0oC)
(all hr yr-1)
Fraction of
nocturnal hours
with low wind
(u*<0.3ms-1)
(calm hr all hr-1)
Difference
in CO2 efflux
high vs low wind
(kg ha-1 hr-1)
Annual
Correction
(kg ha-1 yr-1)
NOBS
km83
0.54
0.92
1400
4000
0.5
2.5
9000
400
X
X

## Slide 45
Most nights at km 83 are calm
Incidence of nocturnal u*
km 83
NOBS

## Slide 46: Representativeness
Tons, hectares, kg, meters …
  1 t = 103 kg
  1 ha = 104 m2
Km 83 tower takes up 1 to 9 t ha -1 yr-1, depending on threshold value for u* filter
Area of tropical forest in South America ~ 109 ha
If this tower were representative, Amazon Basin would be a sink of 1 to 9 GtC yr-1!
The neighboring tower (km 67) in old-growth rainforest is a source of CO2